## Slide 1: Secure Communication for Signals
Paul Cuff
Electrical Engineering
Princeton University

## Slide 2: Information Theory
Secrecy
Source
Channel
Secrecy
Source Coding
Channel Coding

## Slide 3: Main Idea
Secrecy for signals in distributed systems
  Want low distortion for the receiver and high distortion for the eavesdropper.
  More generally, want to maximize a function
Node A
Node B
Message
Information
Signal
Action
Adversary
Distributed System
Attack
Notes: Special Cases: rate-distortion theory (no adversary); lossless (Globecom); unlimited secret key; unlimited communication; seperability of nodes B and C.

## Slide 4: Communication in Distributed Systems
“Smart Grid”
Image from http://www.solarshop.com.au

## Slide 5: Example: Rate-Limited Control
Adversary
00101110010010111
Signal (sensor)
Communication
Signal (control)
Attack Signal

## Slide 6: Example: Feedback Stabilization
Data-rate Theorem [Baillieul, Brockett , Mitter, Nair, Tatikonda, Wong]
Controller
Dynamic System
Encoder
Decoder
10010011011010101101010100101101011
Sensor
Adversary
Feedback

## Slide 7: Traditional View of Encryption
Information inside

## Slide 8: A Brief History of Crypto
Substitution Cipher to Shannon and Hellman

## Slide 9: Cipher
Plaintext: Source of information:
  Example: English text: Information Theory
Ciphertext: Encrypted sequence:
  Example: Non-sense text: cu@ist.tr4isit13
Encipherer
Decipherer
Ciphertext
Key
Key
Plaintext
Plaintext

## Slide 10: Example: Substitution Cipher
Alphabet | A B C D E …
Mixed Alphabet | F Q S A R …
Simple Substitution
  Example:
    Plaintext: …RANDOMLY GENERATED CODEB…
    Ciphertext: …DFLAUIPV WRLRDFNRA SXARQ…
Caesar Cipher
Alphabet | A B C D E …
Mixed Alphabet | D E F G H …
Notes: Julius Caesar used this cipher, with a shift of 3. His nephew, Augustus, used a shift of 1.

## Slide 11: Shannon Analysis
1948
  Channel Capacity
  Lossless Source Coding
  Lossy Compression
1949 - Perfect Secrecy
  Adversary learns nothing about the information
  Only possible if the key is larger than the information

## Slide 12: Shannon Model
Schematic
Assumption
  Enemy knows everything about the system except the key
Requirement
  The decipherer accurately reconstructs the information
Encipherer
Decipherer
Ciphertext
Key
Key
Plaintext
Plaintext
Adversary
For simple substitution:
Notes: 26! Is about 4 x 10^26 (the number of atoms in my chair). 88.4 bits
Redundancy of English is about 3.75 5bits per letter. (without spaces it’s 3.7)
About 25 letters needed to decode

## Slide 13: Shannon Analysis
Equivocation vs Redundancy
  Equivocation is conditional entropy:
  Redundancy is lack of entropy of the source:
  Equivocation reduces with redundancy:

## Slide 14: Computational Secrecy
Assume limited computation resources
Public Key Encryption
  Trapdoor Functions
Difficulty not proven
  Can become a “cat and mouse” game
Vulnerable to quantum computer attack
1 125 897 758 834 689
524 287
2 147 483 647
X

## Slide 15: Information Theoretic Secrecy
Achieve secrecy from randomness (key or channel), not from computational limit of adversary.
  Physical layer secrecy (Channel)
    Wyner’s Wiretap Channel [Wyner 1975]
  Partial Secrecy
    Typically measured by “equivocation:”
    Other approaches:
      Error exponent for guessing eavesdropper [Merhav 2003]
      Cost inflicted by adversary [this talk]
Notes: A couple of aspects have been integrated in the study of information theoretic secrecy. One observation is that channel noise can be used, as the key is, to hide the information from an eavesdropper. The other development has been the study of partial secrecy.
Insert a diagram if I have time.

## Slide 16: Equivocation
Not an operationally defined quantity
Bounds:
  List decoding
  Additional information needed for decryption
Not concerned with structure

## Slide 17: Source Coding side of Secrecy
Partial secrecy tailored to the signal

## Slide 18: Our Framework
Assume secrecy resources are available (secret key, private channel, etc.)
How do we encode information optimally?
Game Theoretic Interpretation
  Eavesdropper is the adversary
  System performance (for example, stability) is the payoff
  Bayesian games
  Information structure
Notes: Jam a communication channel; break into a network, counter a military attack; overload a power grid.

## Slide 19: First Attempt to Specify the Problem
Node A
Node B
Message
Key
Information
Action
Adversary
Attack
Encoder:
System payoff: .
Adversary:
Decoder:
Notes: Jam a communication channel; break into a network, counter a military attack; overload a power grid.

## Slide 20: Secrecy-Distortion Literature
[Yamamoto 97]:
  Proposed to cause an eavesdropper to have high reconstruction distortion
[Schieler-Cuff 12]:
  Result: Any positive secret key rate greater than zero gives perfect secrecy.
  Perhaps too optimistic!
  Unsatisfying disconnect between equivocation and distortion.

## Slide 21: How to Force High Distortion
Randomly assign bins
Size of each bin is
Adversary only knows bin
Reconstruction of only depends on the marginal posterior distribution of
Example (Bern(1/3)):

## Slide 22: Competitive Secrecy
Node A
Node B
Message
Key
Information
Action
Adversary
Attack
Encoder:
System payoff: .
Decoder:
Adversary:
Notes: Jam a communication channel; break into a network, counter a military attack; overload a power grid.

## Slide 23: Performance Metric
Value obtained by system:
Objective
  Maximize payoff
Node A
Node B
Message
Key
Information
Action
Adversary
Attack
Notes: Jam a communication channel; break into a network, counter a military attack; overload a power grid.

## Slide 24: Distributed Channel Synthesis
An encoding tool for competitive secrecy

## Slide 25: Actions Independent of Past
The system performance benefits if Xn and Yn are memoryless.

## Slide 26: Channel Synthesis
Black box acts like a memoryless channel
X and Y are an i.i.d. multisource
Source
Output
Q(y|x)
Communication Resources

## Slide 27: Channel Synthesis for Secrecy
Node A
Node B
Information
Action
Adversary
Attack
Channel Synthesis
Not optimal use of resources!

## Slide 28: Channel Synthesis for Secrecy
Node A
Node B
Information
Action
Adversary
Attack
Channel Synthesis
Reveal auxiliary Un “in the clear”
Un

## Slide 29: Point-to-point Coordination
Related to:
  Reverse Shannon Theorem [Bennett et. al.]
  Quantum Measurements [Winter]
  Communication Complexity [Harsha et. al.]
  Strong Coordination [C.-Permuter-Cover]
  Generating Correlated R.V. [Anantharam, Gohari, et. al.]
Node A
Node B
Message
Common Randomness
Source
Output
Synthetic Channel Q(y|x)

## Slide 30: Problem Statement
Canonical Form
Can we design:
such that
Alternative Form
Does there exists a distribution:
f
g

## Slide 31: Construction
Choose U such that PX,Y|U = PX|U PY|U
Choose a random codebook
C
J
K
PX|U
PY|U
Un
Xn
Yn
Cloud Mixing Lemma
[Wyner], [Han-Verdu, “resolvability”]

## Slide 32: Theoretical Results
Information Theoretic Rate Regions
Provable Secrecy

## Slide 33: Reminder of Secrecy Problem
Value obtained by system:
Objective
  Maximize payoff
Node A
Node B
Message
Key
Information
Action
Adversary
Attack
Notes: Jam a communication channel; break into a network, counter a military attack; overload a power grid.

## Slide 34: Payoff-Rate Function
Maximum achievable average payoff
Markov relationship:
Theorem:

## Slide 35: Unlimited Public Communication
Maximum achievable average payoff
Conditional common information:
Theorem (R=∞):

## Slide 36: Converse

## Slide 37: Lossless Case
Theorem:
[Cuff 10]
Require Y=X
  Assume a payoff function
Related to Yamamoto’s work [97]
  Difference: Adversary is more capable with more information
Also required:

## Slide 38: Linear Program on the Simplex
Constraint:
Minimize:
Maximize:
U will only have mass at a small subset of points (extreme points)

## Slide 39: Binary-Hamming Case
Binary Source:
Hamming Distortion
Optimal approach
  Reveal excess 0’s or 1’s to condition the hidden bits
0 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1
* | * | 0 | 0 | * | * | 0 | * | 0 | *
Source
Public message

## Slide 40: Binary Source (Example)
Information source is Bern(p)
  Usually zero (p < 0.5)
  Hamming payoff
Secret key rate R0 required to guarantee eavesdropper error
R0
p
Eavesdropper Error

## Slide 41: What the Adversary doesn’t know can hurt him.
[Yamamoto 97]
Knowledge of Adversary:
[Yamamoto 88]:

## Slide 42: Proposed View of Encryption
Information obscured
Images from albo.co.uk