| Summary of Key Features for the three ocean models (HOPS, ROMS and NCOM/ICON) used during the MB06 real-time operations |
| --- |
| Features | HOPS PIs: Allan Robinson robinson@ pacific.deas.harvard.edu Pierre Lermusiaux pierrel@ pacific.harvard.edu | ROMS PI: Yi Chao Yi.Chao @jpl.nasa.gov | NCOM/ICON PI: Igor Shulman Igor.Shulman@ nrlssc.navy.mil |
| Physical modeling component |
| Model Domain | 2-way nested (Mon-Bay/ San Fr. domain and Pt AN domain) Four-corner points: Mon-Bay/San Fr. domain NW: 123.97W, 37.187N NE: 122.53W, 37.876N SW: 122.62W, 35.403N SE: 121.19W, 36.092N Pt AN domain NW: 122.84W, 37.144N NE: 122.33W, 37.389N SW: 122.44W, 36.614N SE: 121.93W, 36.860N 1.5 km and 0.5 km resolutions Grid-point: Mon-Bay /San Fr.: 100x155 Pt AN: 107 x 138 | Inner domain of a 3-level 1-way nested system Four-corner points: NW: 123.58W; 37.432N NE: 122.036W; 37.83N SW: 122.547W; 35.104N SE: 121.048W; 35.57N About 1.5 km resolution in Curvilinear-orthogonal grids Gridpoint:179x83 | NCOM ICON (notation p012) model is one-way coupled to 9km NCOM California Current Model (NCOM CCS), which is one way coupled to 1/8 degree global NCOM model. Four-corner points over water: NW:123.2W, 36.9N NE:122.47W,37.44N SW:122.5W, 35.6N SE:121.43W, 35.86N Curvilinear-orthogonal grid with 1-4 km resolution, 81x53 grid points. NCOM frsICON (notation p022) is one way coupled to NCOM ICON model. Curvilinear-orthogonal grid with 0.5 – 1.5 km res. 114x97 grid |
| Vertical levels | 30 double sigma | 32 stretched sigma | Currently 30 sigma. NCOM ICON version with 41 sigma-Z vertical levels is being tested. |
| Horizontal mixing | Scale-selective Shapiro filter for numerical diffusion | Standard second order diffusion | Smagorinsky formulation |
| Vertical mixing | Vertical: Laplacian mixing, with viscosities and diffusivities estimated using (i) a simple turbulent mixing-layer model from the surface to a ``Ekman’’ depth a function of the local wind-stress and (ii) below this wind mixing layer, a formulation based on Pacanowski and Philander (uses the local gradient Richardson number Ri) | K-Profile Parameterization (KPP) | Mellor-Yamada 2.5 scheme |
| Initial conditions | Multiple initial states and dates have been utilized. Presently, the most successful IC is an initialization on July 27, based on: Synoptic (Mesoscale) state: hydrographic data (Glider, NPS-SST) between Jul 22 2006 and Jul 31 2006 (as available on the COOP web-site on 08-11), with a 3 day de-correlation time. Mean (Larger-scale) state: the above synoptic data and the Pt Sur CTD’s Wecoma CTD’s (up to Aug 8) few GTSSP CTD profiles for July 2006 Initial Surface Elevation & Barotropic Velocities set to sum of the standard geostrophic component and tidal component, and of data-based estimates of the undercurrent and of the CC at the open boundaries of the Mon-Bay-San Fr domain. | Climatology spinup to July 26, 2003 followed by COAMPS forcing | The NCOM ICON was initialized on July 11th of 2006 using fields from the regional model NCOM CCS and spun up with tidal forcing, with COAMPS 3km surface fluxes and with NCOM CCS on open boundaries. Starting from July 21th of 2006 available glider data are being assimilated. |
| Surface forcing |
| Surface wind stress | 3-km COAMPS wind stress; bi-cubically interpolated to HOPS grid | 3-km COAMPS wind at 10-m computed with Large & Pond drag coefficient | 3-km COAMPS wind stress |
| Air-sea heat flux | 3-km COAMPS, bi-cubically interpolated to HOPS grid | 3-km COAMPS radiative heat fluxes, bulk formula for sensible and latent heat fluxes | 3-km COAMPS heat fluxes, short-wave flux penetrates water column. There is option for switch to bulk formulations |
| Air-sea fresh-water flux | 3-km COAMPS precipitation Evaporation derived from COAMPS latent heat flux using: Evap = HeatLatent/(2.5008e6-2.3e3*Tair); Tair from COAMPS. All fields bi-cubically interpolated to HOPS | Climatology | 3-km COAMPS (on or off) |
| River forcing | No | No | No (with the option to turn on) |
| Tides | Yes | Yes; There are three ROMS nowcast/forecast products: (1) 1.5-km ROMS without tides, (2) 1.5-km ROMS with tides, and (3) 600-m ROMS with tides | Yes |
| Open boundary conditions |
| Open ocean boundary conditions | 0.5km Pt AN domain: BCs provided by 1.5km Mon-Bay/San Fr. domain 1.5km Mon-Bay/San Fr. domain: Temp & Salt: combination of mapped data values & Orlanski radiation Internal Velocity: combination of data derived values & Orlanski radiation Surface pressure: combination of data derived values, OTIS tidal fields & Orlanski radiation Barotropic Momentum forcing: combination of data derived values, OTIS tidal fields & Orlanski radiation | 1.5-km ROMS’ BC is provided by 5-km ROMS; 5-km ROMS’ BC is provided by 15-km ROMS; 15-km ROMS’ BC is based on climatology and mixing Orlanski and Flather. | NCOM frsICON model BC are provided by NCOM ICON model. NCOM ICON’BC are provided by NCOM CCS model. NCOMCCS’BC are provided by the NCOM global model |
| Data assimilation |
| Assimilation method | Optimal Interpolation or Error Subspace Statistical Estimation | 3-dimensional variational method (3DVAR) | NRL Ocean Data Assimilation System (NCODA) (Multivariate Data Assimilation) |
| Assimilation window | 12 hours (centered on 11 and 23 GMT, near colder and warmer SST times). | 6 hours at 03, 09, 15, 21 GMT | 12 hourly updates at 00Z and 12Z |
| Observations being assimilated in the reanalysis |
| CTDs | Pt Sur Wecoma Revelle | Pt. Sur | Pt. Sur |
| Gliders | SIO WHOI | SIO WHOI | SIO WHOI ASAP WHOI LOCO |
| NPS Aircraft SST | Yes | Yes | Yes |
| AUVs | Yes (Dorado, RU06) | Yes | Yes |
| Moorings: Temperature & Salinity | No | Yes | No |
| Moorings:ADCP | No | No | No |
| HF radars (CODAR) | No | No | No |
| Satellite data being assimilated in the reanalysis |
| SST | No | Yes, along with AMSR-E for the 15-km ROMS | No in NCOM ICON and NCOM frsICON. The NCOMCCS assimilates T&S profiles and SST from the MODAS system. The MODAS T&S profiles and SST are derived from assimilation of altimeter SSH data; MCSST (Multi-Channel Sea Surface Temperature) and available in-situ T& S profiles. |
| SSH | No | No in 1.5-km ROMS; Yes in 5-km and 15-km ROMS | No in NCOM ICON, or NCOM frsICON. Satellite SSHs are assimilated into the MODAS which is assimilated into the NCOM CCS and the NCOM global models. |
| Model Outputs |
| T, S, u, v (including surface current) provided to MBARI for analysis and comparisons | Yes, netCDF files are provided daily. Each file contains: nowcast through 48-hour forecast fields. Files are provided both at twice daily and hourly time-resolutions. | Yes, netCDF files are provided every 6 hours for nowcast and every 24 hours for the 48-hour forecast fields | Yes (with SSH), netCDF files are provided daily around 9AM PDT with 00Z and 12Z nowcasts &33-hour forecast fields |
| LCS calculation and results | Yes. | Yes. | No |
| Web site with model images and movies | http://oceans.deas.harvard.edu/ASAP/index_ASAP.html | http://ourocean.jpl.nasa.gov/MB06 | http://www7320.nrlssc.navy.mil/ccsnrt |