## Slide 1: Lecture 17: Digital versus analog
LTI system analysis of noise
Noise in circuits
Precision-bandwidth-power (PBP) trade-off
  Precision and bandwidth represent amount of information content in a signal…they cost power to achieve
PBP trade-offs in digital vs. analog
  Power cost of precision scales according to different trend lines

## Slide 2: Digital power consumption
Dynamic Power
Switching power: due to charging and discharging of caps
Short-circuit power: due to PMOS and NMOS simultaneous
conduction from VDD to ground
2) Static Power
Sub-Vt leakage: due to MOSFET conduction when VGS=0,
Gate leakage: charge from the channel region can cross
the gate oxide
Junction leakage: reversed biased diodes (e.g., in S/D)
leak current

## Slide 3: Analog/digital power & area scaling
Courtesy R. Sarpeshkar