## Slide 1: Lecture 3: The MOSFET I
Amplifiers give us gain for SNR, feedback
Freq. characteristics help for instrumentation and computation
Semiconductors provide some useful in-out
transfer functions
  How can we use these for computation
How does a MOSFET work
  Trade-offs: energy sources and performance

## Slide 2: Density of possible states
Density of states function g(E)
Intrinsic:
Doped:
Fermi-Dirac distribution function f(E)
E.g., Number of electrons:
Probability of electron at energy E
Density of states available at E
Courtesy
D. Pulfrey

## Slide 3: Building a MOSFET
4 Terminal:

## Slide 4: Threshold Voltage
Sub-Vt
E-field (from gate) pushes away holes and exposes ions (i.e., E-field penetrates substrate)
→ causes voltage drop on Cdep
Above Vt
Substrate voltage drop allows in electrons from S/D (rapidly!)
→ E-field ends at surface,
no more voltage across Cdep

## Slide 5: MOSFET Sub-Vt Characteristics
Carrier density
Energy level
Carrier concentration
Source current
Drain current
Vchannel (depends on VG through cap divider)
Lateral distance
VSOURCE
VDRAIN
Concentration
Depends exponentially on VCH-VDRAIN
Is too low to affect channel voltage
→ diffusion current

## Slide 6: MOSFET Sub-Vt Characteristics
VDB ≈ (4 to 5) x kT/q

## Slide 7: Above Vt
Carrier density
Energy level
Barrier is reduced; carriers flow freely
(not limited by exponential)
Lots of carriers
(can affect channel voltage)
Free flow of carriers means VDRAIN and VSOURCE significantly set S-D voltage across channel
→Drift current
Caused by voltage drop across channel region