## Slide 1: “Kinetic mechanisms” discussion Summary Matt Oehlschlaeger

## Slide 2: Challenges
Expense of theoretical and experimental determinations of rate coefficient
  ~30 rate theoretical rate predictions / year; similar annual experimental yield
  Not all theoretical predictions are of equal value; QC tools in the wrong hands can be dangerous
Development and optimization of rate rules for reactions that can’t be calculated or measured
  Is number of rules finite?

## Slide 3: Challenges
Never will be enough data to validate a model across all conditions found in a turbulent flame
  Need to identify regimes where uncertainty & sensitivity exists
  Multiple groups perform complimentary experiments
  (Re)evaluate old data
At high temperatures
  Pyroltic chemistry leaves fragments
  Structure of fuel fragments (olefins) controls their reactivity
  Design thoughtful experiment to probe these portions of the models; not always necessary to look at parent fuel
Low temperatures: fuel specific chemistry important
C0 chemistry
  Relatively small uncertainties (~25%)  high cost for small improvements
  HO2 chemistry a question, measurements needed

## Slide 4: Challenges - What does industry care about?
Real fuels
  Blending effects – classes of components
  Prediction of octane rating for fuel blends
  Aromatics, olefins
  N-alkanes (NTC energy release)
  Alternative fuels farther off than public may think
Mechanisms
  Simplicity – number of reactions
  Rate of heat release, transition from low- to high-T, temperature distribution, NOx, soot, noise (diesel), ignition delay
  Resolve trends
  Sensitivity of parameters on operation/performance
Tools for: model development, surrogate formulation, rate prediction, etc.
  Methods for dissemination and training
  Industry is using: not predictive enough for computer design
    No feedback
    Little feedback even between kinetics and CFD communities
  Translation of uncertainties in fundamental properties/predictions to uncertainties in applied outputs (engine performance)

## Slide 5: How has the community changed?
Today’s perception: science will answer everything
1979: Irvin Glassman – “this soot problem keeps coming around”
  Today – soot is still a problem
First n-heptane mechanism ~1970
  Still being worked on
  First N-dodecane mechanism ~1990s
    Similar fidelity to n-heptane
  Still work need – NTC/low-T regions
Our work is directed by the problems facing industry

## Slide 6: Roadmap/Collaborations
Common community C0 model
  Optimized vs not
  Dynamic vs fixed vs partially fixed
Documentation
  Data must be made available – necessary for simulation of exp
  Models must be available, documented, and consistent (e.g., forward and reverse rates consistent with thermo)
  Should further standardization of the requirements for reporting models and experiments exist?
Cyber infrastructure for data/models/etc.
  Models and data need to be on web
    Improve the visibility of our work
    Historical record of model changes
  Prime?